## Slide 1: Lab 02 Open Virtual Switch (Open vSwitch)
CEG5101 Modern Computer Networking
Graduate Assistant: Mr. Binghui Wu (e0675868@u.nus.edu) and Ms. Divya D Kulkarni, (e0974142@u.nus.edu),
Prepared by: Ms. Anum Talpur (Ex-Graduate Assistant)
Lecturer: Assoc. Prof. Mohan Gurusamy
ECE Department, CDE., National University of Singapore

## Slide 2: Class Activity
To become familiar with Open vSwitch and its basic operation
To implement Open vSwitch flow tables
To enable traffic forwarding using layer 3

## Slide 3: Class Activity
To become familiar with Open vSwitch and its basic operation
To implement Open vSwitch flow tables
To enable traffic forwarding using layer 3

## Slide 4: Introduction
Open vSwitch, abbreviated as OVS, is a virtual multilayer switch
Working with virtualization and cloud technologies
Used in virtual management system to enable network automation through programmatic extension
Service for controlling network connections between virtual machines (VMs)
https://www.openvswitch.org
Notes: Open vSwitch offers a strong service for controlling network connections between VMs running in highly dynamic, multiserver environments such as the cloud. With Open vSwitch, admins get a network control system that can respond and adapt to their systems as they change.
Given its widespread use, it is worth obtaining a basic understanding of Open vSwitch, especially for those working with virtualization and cloud technologies.
Open vSwitch is a Linux Foundation collaborative project

## Slide 5: Introduction
Legacy Switch
Open vSwitch
Secure fail-mode
Standalone fail-mode

## Slide 6: Class Activity
To become familiar with Open vSwitch and its basic operation
To implement Open vSwitch flow tables
To Enable traffic forwarding using layer 3
Topology (demo)
Assign 10.0.0.1/8 and 10.0.0.2/8 to host h1 and h2, respectively
Run the network
Notes: If the OVS fail mode is set to "secure", the switch will only forward packets according to how its flow table is currently programmed. If a packet does not match any flow, it will be dropped.
If the OVS fail mode is set to "standalone", the switch will mimic a learning switch and forward packets automatically between switch ports.

## Slide 7: Class Activity
To become familiar with Open vSwitch and its basic operation
To implement Open vSwitch flow tables
To Enable traffic forwarding using layer 3
Topology (demo)
check the installed version of Open vSwitch
  sudo ovs-vsctl -V
list all active Open vSwitches
  sudo ovs-vsctl list-br
Verify connectivity
Not working
ovs-vsctl is ovs-vswitched management utility

## Slide 8: Class Activity
To become familiar with Open vSwitch and its basic operation
To implement Open vSwitch flow tables
To enable traffic forwarding using layer 3

## Slide 9: Class Activity
To become familiar with Open vSwitch and its basic operation
To implement Open vSwitch flow tables
To Enable traffic forwarding using layer 3
Topology (demo)
Task:
Command:
  sudo ovs-ofctl [TASK] [NAME_SWITCH] [ACTION]
ovs-ofctl is monitoring and administering utility
dump-flows | List available flows
add-flow | Add flow within flow table
del-flows | Delete flows from flow table
1
2
3

## Slide 10: Class Activity
To become familiar with Open vSwitch and its basic operation
To implement Open vSwitch flow tables
To Enable traffic forwarding using layer 3
Topology (demo)
Task:
Command:
  sudo ovs-ofctl [TASK] [NAME_SWITCH] [ACTION]
  Verify connectivity
ovs-ofctl is monitoring and administering utility
dump-flow | List available flows
add-flow | Add flow within flow table
del-flows | Delete flows from flow table
sudo ovs-ofctl add-flow s5 action=normal
sudo ovs-ofctl dump-flows s5
Traditional
switch
forwarding

## Slide 11: Class Activity
To become familiar with Open vSwitch and its basic operation
To implement Open vSwitch flow tables
To enable traffic forwarding using layer 3

## Slide 12: Class Activity
To become familiar with Open vSwitch and its basic operation
To implement Open vSwitch flow tables
To Enable traffic forwarding using layer 3
Topology (demo)
Task:
Manual entries using layer-3 info:
  First, verify which port of the switch is connected to which host?
  sudo ovs-ofctl [TASK] [NAME_SWITCH] [ACTION]
ovs-ofctl is monitoring and administering utility
dump-flow | List available flows
add-flow | Add flow within flow table
del-flows | Delete flows from flow table
sudo ovs-ofctl add-flow s5 ip,nw_dst=10.0.0.1,action=output:1
.
.
sudo ovs-ofctl add-flow s5 arp,action=normal

## Slide 13: Class Activity
To become familiar with Open vSwitch and its basic operation
To implement Open vSwitch flow tables
To Enable traffic forwarding using layer 3
Topology (demo)
Actions:
Verify flow tables – dump-flows
Verify connectivity - ping
ovs-ofctl is monitoring and administering utility
dump-flows | List available flows
add-flow | Add flow within flow table
del-flows | Delete flows from flow table
We can work with src IP instead of destination
sudo ovs-ofctl add-flow s5 ip,nw_src=10.0.0.1,action=output:2
.
.
sudo ovs-ofctl add-flow s5 arp,action=normal

## Slide 14: Class Activity
Use different information (different layer data) to enables forwarding
Topology (demo)
Actions:
sudo ovs-ofctl [TASK] [NAME_SWITCH] [ACTION]
Layer 1: Use physical ports
  sudo ovs-ofctl add-flow s5 in_port=1,action=output:2
  sudo ovs-ofctl add-flow s5 in_port=2,action=output:1
Layer 2: Use mac address
  sudo ovs-ofctl add-flow s5 dl_dst=XXXXXXXXX,action=output:1
  sudo ovs-ofctl add-flow s5 dl_dst=XXXXXXXXX,action=output:2
  sudo ovs-ofctl add-flow s5 arp,action=normal
ovs-ofctl is monitoring and administering utility
dump-flows | List available flows
add-flow | Add flow within flow table
del-flows | Delete flows from flow table

## Slide 15: References
https://www.openvswitch.org – Open Virtual Switch
http://mininet.org/ - Basics and Installation
http://www.openvswitch.org//support/dist-docs/ovs-ofctl.8.txt - ovs-ofctl command help