## Slide 1: Lab 03 Software-Defined Network (SDN) with POX Controller
CEG5101 Modern Computer Networking
Graduate Assistant:Mr. Binghui Wu (e0675868@u.nus.edu) and Ms. Divya D Kulkarni (e0974142@u.nus.edu)
Prepared by: Ms. Anum Talpur (Ex-Graduate Assistant)
Lecturer: Assoc. Prof. Mohan Gurusamy
ECE Department, CDE., National University of Singapore

## Slide 2: Class Activity
To become familiar with the concept of SDN and Controller.
To download and install the POX controller.
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.

## Slide 3: Class Activity
To become familiar with the concept of SDN and Controller.
To download and install the POX controller.
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.

## Slide 4: Introduction
SDN or software-defined networking is a concept in which application programming interfaces (APIs) are used to enable intelligence within the network.
SDN decouples the control plane from the data plane and implements it as software instead to enable flexibility within a network through programmatic access.
The data plane is the part of the network which handles traffic forwarding and the control plane is the part that instructs or configures the data plane on the traffic forwarding process.
In this lab activity, we will learn to use a controller to update data forwarding rules on the Open vSwitch (OVS) to enable communication between different hosts/machines.

## Slide 5: Class Activity
To become familiar with the concept of SDN and Controller.
To download and install the POX controller.
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.
Page 02

## Slide 6: Class Activity
To become familiar with the concept of SDN and Controller.
To download and install the POX controller.
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.

## Slide 7: Class Activity
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.
POX Controller
  POX controller is a python-based controller platform that allows fast prototyping and controlling of the network using stock components that are pre-programmed.
  The stock components provide different functionalities and features and are listed on GitHub*.
  It comes with a handful of components, but POX’s target audience is really people who want to be developing their own.
https://noxrepo.github.io/pox-doc/html/#stock-components

## Slide 8: Class Activity
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.
Topology (demo)
Start a POX controller and run the network
  forwarding.l2_learning
sudo ./pox.py [stock component] [parameter]
Device | IP Address | Port Number
c0 | 127.0.0.1 | 6633
h1 | 10.0.0.1 | -
h2 | 10.0.0.2 | -
h3 | 10.0.0.3 | -
h4 | 10.0.0.4 | -
*remote controller
* Start CLI
cd pox
sudo ./pox.py forwarding.l2_learning

## Slide 9: Class Activity
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.
Topology (demo)
Check OVS flow table entries
  Using ovs-ofctl utility
Test Connectivity
  tcpdump on 3 hosts and ping from 1 host
Check OVS flow table entries again
Device | IP Address | Port Number
c0 | 127.0.0.1 | 6633
h1 | 10.0.0.1 | -
h2 | 10.0.0.2 | -
h3 | 10.0.0.3 | -
h4 | 10.0.0.4 | -
*remote controller

## Slide 10: Class Activity
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.
Topology (demo)
Start a POX controller and run the network
  forwarding.hub (flooding)
Device | IP Address | Port Number
c0 | 127.0.0.1 | 6633
h1 | 10.0.0.1 | -
h2 | 10.0.0.2 | -
h3 | 10.0.0.3 | -
h4 | 10.0.0.4 | -
*remote controller
cd pox
sudo ./pox.py forwarding.hub

## Slide 11: Class Activity
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.
Topology (demo)
Test Connectivity
  tcpdump on 3 hosts and ping from 1 host
Check OVS flow table entries
  Using ovs-ofctl utility
Device | IP Address | Port Number
c0 | 127.0.0.1 | 6633
h1 | 10.0.0.1 | -
h2 | 10.0.0.2 | -
h3 | 10.0.0.3 | -
h4 | 10.0.0.4 | -
*remote controller

## Slide 12: Class Activity
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.
Topology (demo)
Start a POX controller and run the network
  Misc.ip_loadbalancer (balance the load among servers)
sudo ./pox.py [stock component] [parameter]
Device | IP Address | Port Number
c0 | 127.0.0.1 | 6633
h1 | 10.0.0.1 | -
h2 | 10.0.0.2 | -
h3 | 10.0.0.3 | -
h4 | 10.0.0.4 | -
*remote controller
cd pox
sudo ./pox.py misc.ip_loadbalancer --ip=10.0.10.1
--servers=10.0.0.1,10.0.0.2

## Slide 13: Class Activity
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.
Topology (demo)
Test Connectivity
  Start tcp servers and send data from client to server using curl
Device | IP Address | Port Number
c0 | 127.0.0.1 | 6633
h1 | 10.0.0.1 | -
h2 | 10.0.0.2 | -
h3 | 10.0.0.3 | -
h4 | 10.0.0.4 | -
*remote controller
SERVER : python –m http.server 80
CLIENT : curl 10.0.10.1

## Slide 14: Class Activity
To invoke the POX controller as a layer-2 learning switch.
To invoke the POX controller as a forwarding hub.
To invoke the POX controller as a load balancer.
Topology (demo)
Check OVS flow table entries
  Using ovs-ofctl utility
Device | IP Address | Port Number
c0 | 127.0.0.1 | 6633
h1 | 10.0.0.1 | -
h2 | 10.0.0.2 | -
h3 | 10.0.0.3 | -
h4 | 10.0.0.4 | -
*remote controller

## Slide 15: Assignment Problem

## Slide 16: References
https://noxrepo.github.io/pox-doc/html/#stock-components – POX Controller
http://mininet.org/ - Basics
https://docs.python.org/3/ - Python